## Slide 1
DIPARTIMENTO DI INGEGNERIA ELETTRICA E TECNOLOGIE DELL’INFORMAZIONE
SCUOLA POLITECNICA E DELLE SCIENZE DI BASE
Field and Service Robotics project
Motion planning and control of car-like robot
Maisto Paolo, Vittozzi Angelo
MASTER'S DEGREE IN AUTOMATION ENGINEERING AND ROBOTICS
Weston Robot - Robot SCOUT MINI

## Slide 2
2/28
Index
Introduction
  Car-like robot: kinematic modeling
Motion planning
  PRM, BFS and path smoothing
  Reeds-Shepp Curves and Dijkstra's algorithm
Input-Output Linearization control
Simulations and results

## Slide 3
3/28
Car-like robot: kinematic modeling
Two nonholonomic constraints, one for each wheel (pure rolling constraints)
Using rigid-body constraints
Pfaffian constraint matrix
Kinematic model (rear-wheel driving)
the second kinematic constraint becomes

## Slide 4
INPUT-OUTPUT LINEARIZATION CONTROL
4/28
Goals
MOTION PLANNING
A smooth path planning algorithm is implemented for car-like robot and determine trajectory. Two algorithms are implemented:
PRM, BFS and path smoothing method
Reeds-Shepp Curves with Dijkstra’s algorithm
Given the trajectory in the previous point, an Input/Output Linearization control approach is implemented to control the position of car-like robot.

## Slide 5
5/28
Occupancy map creation
Creation occupancy map from image with MATLAB
0  cell with an obstacle
1  free cell

## Slide 6
6/28
Motion planning: goals
Path planning (find path from to with an algorithm)
Obstacle avoidance
Respect to nonholonomic constraints of car-like robot  smooth path
From geometric path, create a desired trajectory in terms of to be given input to the controller
Trajectory
Start point
Goal point

## Slide 7
7/28
Motion planning: 2 approaches
Probabilistic Roadmaps (PRM)
Breadth-first search (BFS)
Smooth path
Path smoothing
Objective:
1
Reeds-Shepp Curves
Dijkstra's algorithm
2

## Slide 8
8/28
Motion planning: 1° approach
Probabilistic Roadmap Method (PRM)
Breadth-First Search (BFS)
Path smoothing
Probabilistic Roadmaps (PRM)
Breadth-first search (BFS)
Path smoothing
1

## Slide 9
9/28
Motion planning: Probabilistic Roadmap Method (PRM)
Next step  find a path with a graph search algorithm
Roadmap construction
1
Graph creation
3
Adding Start and Goal
2
Termination criteria
4
  Sampling
  Collision Checking
  Connecting Nodes

## Slide 10
10/28
Motion planning: Breadth-First Search (BFS)
From PRM  graph that connects the various nodes including the initial and final point
Now the goal is to find the path that allows to go from the start point to the goal point  Breadth-First Search (BFS)
Next step  make the path smooth

## Slide 11
11/28
Motion planning: path smoothing
Path with spline interpolation
Path found with PRM + BFS
Obtained path, which allows to go from the initial point to the final point, is constituted by broken lines
The aim is to make the path smooth in order to eliminate the cusps within the path (as the car-like robot is not able to rotate on itself)  Spline

## Slide 12
12/28
Motion planning: path smoothing
Path with spline interpolation
Path found with PRM BFS

## Slide 13
13/28
Motion planning: obstacle collision check
Another candidate found path
Obstacle-free smooth path
A candidate found path
Smooth path intersecting obstacles

## Slide 14
14/28
Motion planning: 2° approach
Reeds-Shepp Curves
Dijkstra's algorithm
2

## Slide 15
15/28
Motion planning: Reeds-Shepp Curves
Circular arcs of varying lengths traversed with velocities:
The radius of these circular arcs is determined by
Linear segments of varying lengths traversed with velocities:
No cusps because the movement is always forward.
Dubins Curves
Next step  find the optimal path with an optimization algorithm
The curves are designed to satisfy the kinematic constraints of the robot, considering only certain motion primitives ( and for circular arcs and for linear segments).
Velocity limits:

## Slide 16
16/28
Motion planning: Dijkstra's algorithm
Find neighbors
1
Select next node & repeat
3
Update distance costs
2
Termination criteria
4
Notes: The steps of Dijkstra’s algorithm are as follows:
Initialize distances:
  Set the distance to the source vertex 𝑠 to 0: 𝑑(𝑠)=0;
  Set the distance to all other vertices to infinity: 𝑑(𝑣)=∞ for all 𝑣∈𝑉, 𝑣≠𝑠;
Initialize a priority queue 𝑄 and insert all vertices 𝑣 with their corresponding distances 𝑑(𝑣);
While 𝑄 is not empty:
  Extract the vertex 𝑢 from 𝑄 with the smallest distance 𝑑(𝑢);
  For each neighbor 𝑣 of 𝑢 (i.e., for each edge (𝑢,𝑣)∈𝐸):
    Calculate the potential new path distance: 𝑑_𝑛𝑒𝑤=𝑑(𝑢)+𝑤(𝑢,𝑣), where 𝑤(𝑢,𝑣) is the weight of the edge (𝑢,𝑣);
    If 𝑑_𝑛𝑒𝑤<𝑑(𝑣):
      Update 𝑑(𝑣)=𝑑_𝑛𝑒𝑤​;
      Decrease the priority of 𝑣 in 𝑄;

## Slide 17
17/28
Motion planning: trajectory
Create desired trajectory in terms of to be given input to the controller
From geometric path
Adding time law
Points representing the geometric path in terms of and coordinates was provides from path planning;
1
2
Time law was defined as a function that maps time to the arclength . Fit a polynomial of degree 7 to map time to the arclength. polyfit and polyval functions in MATLAB was used.
4
3
Trajectory: and
Time law is used to remap the values of the geometric path and . interp1 function with the spline option in MATLAB was used.
TRAJECTORY = PATH + TIME LAW

## Slide 18
INPUT-OUTPUT LINEARIZATION CONTROL
18/28
Goals
MOTION PLANNING
A smooth path planning algorithm is implemented for car-like robot and determine trajectory. Two algorithms are implemented:
PRM, BFS and path smoothing method
Reeds-Shepp Curves with Dijkstra’s algorithm
Given the trajectory in the previous point, an Input/Output Linearization control approach is implemented to control the position of car-like robot.

## Slide 19
19/28
Input-Output Linearization control
The output choice for the trajectory tracking task is:
System output is redefined as:
Heading velocity and angular velocity:
Controller
The time derivatives of these outputs (substituting the kinematic model of the car-like robot) :
 coordinates of midpoint of the axle of rear wheels
 coordinates of the point P
Since , we can set:

## Slide 20
20/28
Input-Output Linearization control
Desired trajectory
Outputs
Desired outputs
Velocities
Virtual control inputs
Current states
Current states

## Slide 21
21/28
Input-Output Linearization control
PRM + BFS
RSC + Dijkstra

## Slide 22
22/28
Simulations and Results: 1° approach
Found path with PRM + BFS
Smoothed path
Desired trajectory in MATLAB
Desired trajectory in SIMULINK
Performed trajectory in SIMULINK

## Slide 23
23/28
Simulations and Results: 1° approach
Error of
Error of
Error of
Error of

## Slide 24
24/28
Simulations and Results: 1° approach
Heading velocity and angular velocity in MATLAB
Heading velocity and angular velocity in SIMULINK

## Slide 25
25/28
Simulations and Results: 2° approach
Optimal path
Desired trajectory in MATLAB
Desired trajectory in SIMULINK
Performed trajectory in SIMULINK

## Slide 26
26/28
Simulations and Results: 2° approach
Error of
Error of
Error of
Error of

## Slide 27
27/28
Simulations and Results: 2° approach
Heading velocity and angular velocity in MATLAB
Heading velocity and angular velocity in SIMULINK

## Slide 28
28/28
Thank you for your attention !!